## Slide 1: Swerve Drive Software Design

## Slide 2: Software Layers
Joystick Axis Correction
Joystick Response Calculation
Field-oriented Angle Adjustment
Swerve Drive Steer Angle / Drive Speed Calculation
L F
R F
L B
R B
Steer Motor PID
Controllers
L F
R F
L B
R B
Drive Motor PID
Controllers
Motor/Wheel Orientation Adjustments

## Slide 3: Software Tuning
Steering Angle Sensor Offsets
P
I
D
Steer PID
Tuning
P
I
D
F
Drive PID
Tuning
Joystick Response Tuning
Motor/Wheel Orientation Settings

## Slide 4: Motor/Wheel Orientation Normalization
Steering Motors are mounted upside-down, Angle Sensors are mounted rightside-up.
  Setpoint angles need to be inverted
Drive Motors are inverted on the left and right-side of the robot.
Some motors rotate “backwards”
Drive Motor Gear Ratios are not 1:1

## Slide 5: Joystick Axis Correction
Flight Joysticks have Y forward as “dive”, so Y forward is NEGATIVE.
  Drive Joysticks need to invert the Y axis.

## Slide 6: Joystick Response Calculation
When Joysticks are at rest, they don’t read exactly 0 (in X, Y and Twist Axes).
  A “deadband” is needed, otherwise the Robot will “twitch” when the joystick is centered.
Humans find non-linear joystick response (less-sensitive near the middle) easier to use.
X/Y -> .4x^3+.6x
Rot -> .7 * (.4x^3+.6x)

## Slide 7: Field-Oriented Angle Adjustment
It’s simpler to drive an omniwheel system if joystick straight ahead is ALWAYS aligned with the field – even if the robot body is rotated.
  It’s much simpler if rotating the robot doesn’t change the direction the joystick will move the robot.
Field-oriented drive reads the angular offset between robot’s current rotation and “north” on the field – using data from the IMU.
Then, software rotates the X/Y joystick directions by this difference.

## Slide 8: Swerve-Drive Steer Angle/Drive Speed Calculation
Translates X, Y and Rotation Values into Steering Motor Angles and Drive Motor Velocities.
Steering Motor Angles are a “mix” of the X/Y angle, and a rotation angle (which is only present if Rotation != 0)

## Slide 9: Steer Motor PID Controllers
Uses Angle Sensor (-180 to 180 degrees) as Input.
Outputs to Motors (-1 to 1).
Uses Proportional (P), Integral (I) and D (Differential) coefficients, which require tuning.
Operates 50 times per second.
Each steering motor has it’s own PID controller.
Fast, accurate operation is crucial to smooth performance.

## Slide 10: Drive Motor PID Controllers
Uses RPM Sensor (360 ticks per revolution) as Input.
Outputs to Motors (-1 to 1).
Uses Proportional (P), Integral (I) and D (Differential) coefficients, which require tuning.
Operates 50 times per second.
Each drive motor has it’s own PID controller.
Required for high-accuracy autonomous “drive this far” commands, to ensure similar behavior at different battery levels, and to account for differing amount of wheel slip.

## Slide 11: Joystick Response Tuning
Software adjusts the magnitude of the X, Y and Rotation values so it “feels” responsive to a human.
Autonomous code has no need for this correction.
This is an interactive process; here’s the curve that Lexa developed in the 2012 season for the mecanum robot.
We later adjusted this to slow down the robot we finally built, but unfortunately didn’t create a graph of this curve.

## Slide 12: PID Coefficient Tuning
Simplest thing is P only.
If P doesn’t quite get there, we add an I.
If P overshoots, we can decrease P and increase D.
It’s not as easy as it sounds, and takes some time.